|  | Injury & Illness Prevention Program Job Safety Analysis Form |
| --- | --- |

| Picture of task/equipment: | Task: | Municipal trash |
| --- | --- | --- |
|  | Name of Shop or Dept: | OCH-Rooms |
|  | Job Title(s): | Custodian, Assistant & Senior |
|  | Analyzed by: | M. Williams |
|  | Date: | 05/09/13 |
| Required PPE: |
| Non-Slip shoes Neoprene (thick) gloves |
| Required/Recommended Trainings: |
| STF Safety Ergonomics |
| TASK | HAZARDS | CONTROLS |
| Manual trash handling | Lacerations Punctures Slips Trips Falls Sprains Strains | Don PPE, including non-slip shoes and gloves prior to handling trash. Visually look over the contents of the trash to make sure nothing is protruding from the can that can cause injury Check the weight of the trash can by tilting or tapping it, if the bag is too heavy avoid lifting straight up. For heavy loads tilt the trash can down to eliminate the need to pull trash vertically. Use proper lifting techniques. Bend your knees, keep close to the waste can and keep your back straight as you pick up or lower trash cans. Remain upright while relining the trash cans, avoid bending at the back. Whenever possible, use both hands to pick up and lower trash cans. For small office trash cans one hand can be used, but alternate hands whenever possible, especially when emptying a high frequency of offices. Never manually push the trash down with your hands as there may be sharp objects. Remember to think before you lift and focus on the specific task. |