|  | Injury & Illness Prevention Program Job Safety Analysis Form |
| --- | --- |

| Picture of task/equipment: | Task: | Vehicle Battery Removal/Installation |
| --- | --- | --- |
|  | Name of Shop or Dept: |  |
|  | Job Title(s): |  |
|  | Analyzed by: |  |
|  | Date: |  |
| Required PPE: |
| Work Gloves Safety Glasses Closed Toe Shoes |
| Required/Recommended Trainings: |
| Materials Handling Safe Lifting/Back Safety |
| TASK | HAZARDS | CONTROLS |
| 1. Restrain Wheels | Cart can roll away | Chock Wheels |
| 2. Remove Obstructions | Strain injuries due to awkward movements when removing batteries | Remove all braces, cables & obstructions blocking battery removal DO NOT remove battery without first removing braces, cables and other obstructions |
| 3. Put battery lift into position | Trips/Falls | Move battery lift into position near vehicle Slide feet of battery lift under vehicle Watch your step Move crane into the vehicle |
| 4. Attach battery to battery lift crane | Dropped battery | Inspect battery handle for wear If worn or damaged, attach a battery terminal grabber (see second picture) Attach crane hook to lift the battery |
| 5. Remove Batteries with battery lift | Strain injuries due to awkward movements when removing batteries | Use IN/OUT switch on battery lift to operate battery lift. OUT position will cause crane to start lifting the battery. Carefully lift battery out of vehicle Guide crane with your hands to direct battery out of compartment DO NOT lift the battery manually Keep face away from lift crane hook Move crane arm out of vehicle to desired position IN position of switch will gradually lower the battery to the ground Unhook battery handle from crane |