|  | Injury & Illness Prevention Program Job Safety Analysis Form |
| --- | --- |

| Picture of task/equipment: | Task: | Walk behind push mower |
| --- | --- | --- |
|  | Name of Shop or Dept: | OCH-Grounds, LACC & UA |
|  | Job Title(s): | Groundskeepers, Maintenance staff |
|  | Analyzed by: | M. Williams |
|  | Date: | 03/08/13 |
| Required PPE: |
| Work boots Gloves hearing protection safety glasses dust mask Safety vest |
| Required/Recommended Trainings: |
| STF Safety Equipment safety precautions |
| TASK | HAZARDS | CONTROLS |
| Operating a push mower | Slips Trips Falls Lacerations Amputations Struck-by’s Burns Hearing loss | Don PPE before starting equipment, including non-slip work boots, Gloves, Hearing Protection, Safety glasses, a mask and a safety vest (when working near public roadways). Make sure all guards and collection bag are in place before operating equipment. Gas vapors are extremely flammable, only refill tank outdoors, in well ventilated areas. Make sure engine is off when refilling. Inspect area to be mowed for debris, such as sticks, wires, sprinkler heads, rocks, etc. Remove all debris prior to starting mower. Always keep clear of rotating blades. Blades will cut and can amputate fingers, hands, toes or feet. Never reach in or under mower while it is in the “on” position. When mowing on inclines, move across not up and down slopes. Watch for uneven surfaces, holes and slopes; take extra care with footing to avoid STF’s. Remember to look down and behind when it is necessary to walk backwards with the mower. Do not touch muffler while in operation. Muffler will become very hot and can cause burns. |